## Slide 1: BIM - ISO 19650 Overview and Implementation
Paul Vesey

## Slide 2: BIM - Process or Technology?
BIM is a Technology Enabled Process

## Slide 3: Building Blocks of BIM
Building Data
Design & Specification
Construction Process & Methodologies
Communications
Digital, Analogue, Interpersonal

## Slide 4: Building Design & Specification
Well Established

## Slide 5: Construction Processes
Well known and understood, but continually evolving

## Slide 6: Communications
Remain problematic
Many actors
Differing technologies
Information Locations
Information Latency

## Slide 7: Construction Inefficiency
Deficient Planning
Design Error & Change
Communication Latency
Poor On-site Productivity & Task Tracking
Etc.

## Slide 8: How does BIM help?
Fundamental Concepts from Manufacturing Sector
Highly detailed digital models of the built asset

## Slide 9: Why is BIM Necessary?
Designs Resolved Earlier
Manufacturability (Constructability) addressed earlier
Better understanding of the design by all parties

## Slide 10: Key Features of BIM Process
Detailed Documentation earlier in the project
Clash Detection carried out on Digital Models
Support Activities can be modelled earlier
  Material Supply, Storage and Movement
  Formwork
  Health & Safety

## Slide 11: How to Utilize BIM
Not Possible without Management Planning
Technology is not enough
Detailed Processes needed for BIM management and control

## Slide 12: Key Features of BIM Project Delivery
Common Data Environment (CDE)
Clear Understanding of the Client (Building Owner) Requirements for both the Build Project and Asset Management post construction
Client must clearly define their information needs before the project starts
Supply Chain Must understand their part in ensuring the project meets both the Asset Requirements and the Information Requirements
ISO19650 seeks to create a framework for these needs to be met

## Slide 13: ISO 19650
International Organization for Standardization
ISO19650 is a Global standard
Roots in the UK PAS/BS 1192 Standards
ISO19650- Organization and digitization of information about buildings and civil engineering works, including building information modelling (BIM) — Information management using building information modelling
The standard is organized into several interdependent parts
  ISO 19650-1:2018 — Part 1: Concepts and principles
  ISO 19650-2:2018 — Part 2: Delivery phase of the assets
  ISO 19650-3:2020 — Part 3: Operational phase of the assets
  ISO 19650-5:2020 — Part 5: Security-minded approach to information management

## Slide 14: ISO 19650
The standards are not independent
They do not follow in sequence
Part 4 – Information Exchange is under development
  PAS1192 Part 4 (COBie) is available
Part 6 – Health & Safety unknown at this time
  PAS1192 Part 6 is available

## Slide 15: ISO 19650
This lecture will focus on:
  ISO 19650-1:2018 — Part 1: Concepts and principles
  ISO 19650-2:2018 — Part 2: Delivery phase of the assets
  ISO 19650-3:2020 — Part 3: Operational phase of the assets

## Slide 16: ISO 19650 — Part 1: Concepts and principles
Presents a framework for a common understanding
Defines the components of a BIM enabled project delivery platform
Defines some of the key tasks and undertakings of the Client, Main Contractor and Sub-contractors

## Slide 17: Key Terms: Common Data Environment (CDE)
https://bimportal.scottishfuturestrust.org.uk/level2/stage/1/task/2/determine-the-info-management-cde-strategy

## Slide 18: CDE Examples:

## Slide 19: Document Workflow

## Slide 20: Key Terms: Organizational Information Requirements (OIR)
OIR explain the information needed to answer or inform high-level strategic objectives within the appointing party. These requirements can arise for a variety of reasons, including:
  strategic business operation
  strategic asset management
  portfolio planning
  regulatory duties or
  policy-making.
OIR can exist for reasons other than asset management, for example in relation to submitting annual financial accounts. These OIR are not considered further in this document.
Produced by the Client/Employer

## Slide 21: Key Terms: Asset Information Requirements (AIR)
AIR set out managerial, commercial and technical aspects of producing asset information. The managerial and commercial aspects should include the information standard and the production methods and procedures to be implemented by the delivery team.
The technical aspects of the AIR specify those detailed pieces of information needed to answer the asset-related OIR. These requirements should be expressed in such a way that they can be incorporated into asset management appointments to support organizational decision-making.
A set of AIR should be prepared in response to each trigger event during asset operation and where appropriate should also refer to security requirements.
Where there is a supply chain, the AIR received by a lead appointed party can be sub-divided and passed on in any of its own appointments. AIR received by a lead appointed party can be augmented with its own information requirements.
Across an asset management strategy and plan there can exist several different appointments. The AIR from all these should form a single coherent and coordinated set of information requirements, sufficient to address all the asset-related OIR.
Initially produced by the Employer or a Consultant, on behalf of the Employer
Then produced by the Main Contractor for Subcontractors to respond to.

## Slide 22: Key Terms: Project Information Requirements (PIR)
PIR explain the information needed to answer or inform high-level strategic objectives within the appointing party in relation to a particular built asset project. PIR are identified from both the project management process and the asset management process.
A set of information requirements should be prepared for each of the appointing party’s key decision points during the project.
Repeat clients may develop a generic set of PIR that can be adopted, with or without amendment, on all of their projects.
Produced by the Employer, contains project performance information, such as progress reports, project financial information, completion dates, as well as asset information.

## Slide 23: Key Terms: Exchange Information Requirements (EIR)
EIR set out managerial, commercial and technical aspects of producing project information. The managerial and commercial aspects should include the information standard and the production methods and procedures to be implemented by the delivery team.
The technical aspects of the EIR should specify those detailed pieces of information needed to answer the PIR. These requirements should be expressed in such a way that they can be incorporated into project-related appointments. EIR should normally align with trigger events representing the completion of some or all project stages.
EIR should be identified wherever appointments are being established. In particular, EIR received by a lead appointed party can be sub-divided and passed on in any of its own appointments, and so on along the supply chain. EIR received by appointed parties, including lead appointed parties, can be augmented with their own EIR. Some of the EIR can be passed to their own appointed parties, particularly where information exchange within a delivery team is necessary and this information is not to be exchanged with the appointing party.
Across a project there can exist several different appointments. The EIR from all these appointments should form a single coherent and coordinated set of information requirements, sufficient to address all the PIR.
Produced by the employer, the EIR establishes the technical criteria for Project and Asset information to be transmitted.

## Slide 24: Key Terms: Asset Information Model (AIM)
The AIM supports the strategic and day-to-day asset management processes established by the appointing party. It can also provide information at the start of the project delivery process. For example, the AIM can contain equipment registers, cumulative maintenance costs, records of installation and maintenance dates, property ownership details and other details that the appointing party regards as valuable and wishes to manage in a systematic way.
Produced by the Main Contractor in response to the Asset Information Requirements (AIR). Format of the data in accordance with the Exchange Information Requirements (EIR)

## Slide 25: Key Terms: Project Information Model (PIM)
The PIM supports the delivery of the project and contributes to the AIM to support asset management activities. The PIM should also be stored to provide a long-term archive of the project and for auditing purposes. For example, the PIM can contain details of project geometry, location of equipment, performance requirements during project design, method of construction, scheduling, costing and details of installed systems, components and equipment, including maintenance requirements, during project construction.
Produced by the Main contractor with contributions from sub-contractors; best known as the Building Model.

## Slide 27: ISO 19650 — Part 1: Concepts and principles
Presents a framework for a common understanding
Defines the components of a BIM enabled project delivery platform
Defines some of the key tasks and undertakings of the Client, Main Contractor and Sub-contractors

## Slide 28: Key Terms – BIM execution plan (BEP)
plan that explains how the information management aspects of the appointment will be carried out by the delivery team
https://bimcorner.com/creating-a-successful-bim-execution-plan-part-1/

## Slide 29: BEP - BIM Execution Plan

## Slide 30: Key Terms – Task Information Delivery Plan (TIDP)
schedule of information containers and delivery dates, for a specific task team

## Slide 31: Key Terms – Master Information Delivery Plan (MIDP)
plan incorporating all relevant task information delivery plans

## Slide 32: Relationship between MIDP & TIDP

## Slide 33: MPDT - Model Production Delivery Table
https://bimportal.scottishfuturestrust.org.uk/level2/stage/3/task/13/prepare-midp-raci-mp-dt

## Slide 34: Federated Model
https://iopscience.iop.org/article/10.1088/1757-899X/869/2/022038/pdf

## Slide 35: ISO 19650 — Part 2: Part 2: Delivery phase of the assets

## Slide 36: Document Workflow

## Slide 37: Project Delivery and Asset Management

## Slide 38: Project Delivery with no Asset Management

## Slide 39: Asset Management with No Project Delivery

## Slide 40: LOD: Level of Development

## Slide 41: LOD: Level of Development

## Slide 42: The LOD Problem
LOD has led to confusion, primarily due to the differing allocations for the ‘D’
  Level of Development
  Level of Detail
This has somewhat been cleared up by splitting into two alternative approaches
  LOD – Level of Detail, focused on geometric information
  LOI – Level of Information, focused on text-based data

## Slide 43: NBS – Level of Detail / Level of Information
Ref: https://toolkit.thenbs.com/definitions/Ss_65_80_45_72/

## Slide 44: Level of Detail - 2

## Slide 45: Level of Detail - 3

## Slide 46: Level of Detail – 4

## Slide 47: Level of Detail - 5

## Slide 48: Level of Information – 2

## Slide 49: Level of Information – 3

## Slide 50: Level of Information – 4

## Slide 51: Level of Information – 5

## Slide 52: Level of Information – 6

## Slide 53: BIM - ISO 19650 Implementation
Paul Vesey

## Slide 54: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 55: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 56: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 57: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 58: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 59: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 60: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 61: Pulling it all together – Organizational Information Requirements
RIAI - Employers Information Requirements Template Revision P1.2

## Slide 62: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 63: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 64: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 65: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 66: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 67: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 68: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 69: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 70: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 71: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 72: Pulling it all together – BIM Execution Plan
RIAI - BIM Execution Plan Template Revision P1.4

## Slide 73: BIM - Process or Technology?
BIM is a Technology Enabled Process

## Slide 74: BIM - ISO 19650 Overview and Implementation
Paul Vesey