## Slide 1: ‘We don’t need to use 3D Design….’

## Slide 2: Journal Seek

## Slide 3: Basic Project Scheduling Line of Balance
Project Management
Year 4
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 4: Line of Balance
Consider the construction sequence below
Suppose this process is repeated over 8 similar or identical units (for instance houses)
Clearly it would be inefficient to have 8 versions of the construction sequence, all with their own EST’s, LST’s, etc.
For these types of project, ‘Line of Balance’ is selected.
LOB does not replace network logic; it supplements it
A
1
B
2
C
1

## Slide 5: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
First we construct a line
to represent activity A
This line starts at Unit 1 and 1
week later goes through Unit 2,
then U3 etc.
This line represents the start of
activity A on each of the units

## Slide 6: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
We now have the start of each
activity on each unit.
We now need to work out the finish
on each unit
This is done by constructing a
parallel line 1 week after the start
(as the activity duration is 1 week)
Then ‘cap’ it off.
Activity A

## Slide 7: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
If we look at this again, we can see
where the worker assigned to
activity A is at any time.
They start at unit 1, and 1 week
later start on unit 2, unit 3 etc.

## Slide 8: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
Next we need to consider activity B
We assume that the resources are
Different from those assigned to
Activity A
However we do allow a ‘buffer’ of
One week between the activities.
Activity A

## Slide 9: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
We can very quickly
see that activity B is
proceeding at a slower
rate than activity A
The 1 week buffer,
becomes 8 weeks by
unit 8
Activity A
Activity B

## Slide 10: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
Activity A
We can very quickly
see that activity B is
proceeding at a slower
rate than activity A
The 1 week buffer,
becomes 8 weeks by
unit 8

## Slide 11: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
Activity A
Finally, we add activity C
Clearly, this schedule is
inefficient
Activity B
Activity C

## Slide 12: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
Activity A
At present we have a completion at week 20
Activity B is proceeding slower than the other activities.
Considerable time savings could be achieved if Activity B was completed sooner; or brought parallel to activity A and C
We can bring activity B parallel with the others, by increasing the number of resources assigned to B
Activity B
Activity C

## Slide 13: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
Activity A
We double the resources assigned to Activity B
Activity C

## Slide 14: Line of Balance
1
5
4
3
2
6
8
7
Units
Weeks
5
10
15
20
25
Activity A
We double the resources assigned to Activity B
Once Activity B is brought parallel, we can commence activity C earlier without clashing.
By doing this we shorten the overall project duration from 20 weeks to 13 weeks.
Activity C
Activity B
13

## Slide 15: Line of Balance – SS relationship
1
5
4
3
2
6
8
7
Overall Duration
Buffer
Minimum Buffer

## Slide 16: Line of Balance – FF relationship
1
5
4
3
2
6
8
7
Overall Duration
Minimum Buffer
Buffer

## Slide 17: Line of Balance Example 2
Consider the project below which consists of 5 construction activities
The contractor will be constructing 10 houses in the above sequence
Activity | Duration (weeks) | Number of Gangs
Foundations | 2 | 2
External Walls | 4 | 3
Roof Construction | 1 | 1
Internal Finishes | 4 | 3
External Works | 2 | 2
Foundations
2
External Walls
4
Roof
1
Internal Finish
4
External Wrks
2
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 18
The mathematical relationship between the duration of an activity and the number of crews can be expressed as:
For Activity ‘Foundations’ this is
Which means that the last start of ‘Foundations’ is on week 9

## Slide 19: Line of Balance – Example 2
1
5
4
3
2
6
8
7
Number of House Units
Weeks
5
10
15
20
25
10
9
30
35
Foundations
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 20: Line of Balance – Example 2
1
5
4
3
2
6
8
7
Number of House Units
Weeks
5
10
15
20
25
10
9
30
35
Now we consider the external walls
And allow a 1 week buffer between the activities
The activity starts on W3; so last unit will start 12 weeks later on week 15
Foundations
External Walls
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 21: Line of Balance – Example 2
We now need to consider the roof.
It is good practice to run a quick test to determine if the buffer should be applied at the start or end of the activity
We examine the slope of the lines for the External Walls and the Roof
External walls:
Roof:

## Slide 22: Line of Balance – Example 2
External walls:
Roof:
The slope of the ‘External Walls’ activity is 1.33
The slope of the ‘Roof’ activity is 1.00
The lower the number the faster the rate of progress
So in this case we can see that the Roof will progress at a faster rate than the External Walls
Because of this, we need to allow the 1 week buffer at the start of Unit 10; otherwise the program will clash

## Slide 23: Line of Balance – Example 2
1
5
4
3
2
6
8
7
Number of House Units
Weeks
5
10
15
20
25
10
9
30
35
Roof:
We have already determined that the buffer should be allowed on Unit 10 so we draw in the Roof activity
Foundations
External Walls
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 24: Line of Balance – Example 2
1
5
4
3
2
6
8
7
Number of House Units
Weeks
5
10
15
20
25
10
9
30
35
Roof:
We have already determined that the buffer should be allowed on Unit 10 so we draw in the Roof activity
Foundations
External Walls
Roof
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 25: Line of Balance – Example 2
The calculations for each activity can be run at the start of the analysis
It is in fact normal practice to do so..
slope of ‘Roof’: 1.00
slope of ‘Internal Finish’: 1.33; therefore buffer at Unit 1
slope of ‘External Works’: 1.00; therefore buffer at Unit 10
Duration of ‘Internal Finish’: 12 weeks
Duration of ‘External Works’: 9 weeks

## Slide 26: Line of Balance – Example 2
1
5
4
3
2
6
8
7
Number of House Units
Weeks
5
10
15
20
25
10
9
30
35
Foundations
External Walls
External Works
Internal Finish
Roof
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 27: Line of Balance – Example 2
1
5
4
3
2
6
8
7
Number of House Units
Weeks
5
10
15
20
25
10
9
30
35
Foundations
External Walls
External Works
Internal Finish
Roof
Completion on Week 32
Ref: Cooke B and Williams P (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, ISBN 978-1-4051-8380-2

## Slide 28: What else can we determine?
We have determined that completion of unit 10 should occur at the end of week 32
We also have start and end times for all of the activities
Foundations – start week 0: finish week 11
External Walls – start week 3: finish week 19
Roof – start week 11: finish week 21
Internal Finish - start week 13: finish week 29
External Works - start week 21: finish week 32

## Slide 29: What else can we determine?
We can also pin-point progress at any point in time:
For instance at week 15 all foundations should be complete; the last of the external walls should be starting, the roof should be complete on Unit 4, and internal finishes should be 50% complete on Unit 1 and 25% complete on Unit 2

## Slide 30: What else can we determine?
We can also examine the schedule on a particular unit:
Unit 6 should commence on week 5 and be complete by week 28; the roof should be complete by week 17, and any decisions in relation to paint colour etc. must be made by the purchaser before week 19

## Slide 31: Mathematical Method
The solutions presented use a graphical method
Line of balance can also be solved using a mathematical method or algorithm

## Slide 32: Mathematical Method
Construct the Table as shown

## Slide 33: Mathematical Method
Calculate the slope of each balance line using the equation

## Slide 34: Mathematical Method
Compare the slopes
In this case 1.33 is larger than 1.00, therefore the slope goes to the bottom of the graph

## Slide 35: Mathematical Method
An easy way to remember is:
‘the buffer goes to the location of the larger of the two numbers being compared’

## Slide 36: Mathematical Method
In this case the larger number is on the top

## Slide 37: Mathematical Method
So the buffer goes to the top

## Slide 38: Mathematical Method
And so on

## Slide 39: Mathematical Method
And so on…

## Slide 40: Mathematical Method
Add in the total activity durations using

## Slide 41: Mathematical Method
This is the same as:

## Slide 42: Mathematical Method
Now insert the buffers

## Slide 43: Mathematical Method
Foundations start at time 0.00 and finishes 2 days later

## Slide 44: Mathematical Method
Foundations on Unit 10 will start 9 days after the start of Unit 1

## Slide 45: Mathematical Method
Foundations on Unit 1 will finish 2 days later

## Slide 46: Mathematical Method
We have already determined that the buffer between ‘Foundations’ and ‘External Walls’ goes to the bottom

## Slide 47: Mathematical Method
Therefore ‘External Walls’ will commence one day after the finish of ‘Foundations’ on Unit 1; which is Day 3

## Slide 48: Mathematical Method
‘External Walls’ will take 4 days. As this commenced on Day 3, it will be finished 4 days later on Day 7

## Slide 49: Mathematical Method
Unit 10 will start 12 days later on Day 15
And will finish on Day 19

## Slide 50: Mathematical Method
Next we have the roof. The buffer goes to the ‘top’
Therefore we start unit 10 on Day 20 and complete
1 days later on Day 21

## Slide 51: Mathematical Method
Construct the Table as shown

## Slide 52: Mathematical Method
We can now work backwards to determine when
Unit 1 should start and finish

## Slide 53: Mathematical Method
And the process continues on.

## Slide 54: Mathematical Method
And the process continues on.

## Slide 55: Mathematical Method
And the process continues on.

## Slide 56: Mathematical Method
And the process continues on.

## Slide 57: Mathematical Method
Once complete each of the 4 points of the
Balance Line have been determined, so the
diagram can be constructed

## Slide 58: Further Reading
Cooke B. and Williams P. (2009) Construction Planning, Programming & Control, Third Edition, Wiley-Blackwell Publishing, Chapter 9
ISBN 978-1-4051-8380-2

## Slide 59
Next Lectures
  Time Distance
Reading: ‘A Guide to the Project Management Body of Knowledge’ Chapters 5 & 6